## Slide 1: Department of Anesthesia Techniques Title of the lecture: - ESTIMATION OF HEMOGLOBIN by Sahli’s/acid hematin Method Asst.lec.Waleed Khalid Waleedalkhalid85@gmail.com

## Slide 2: Sahli’s/acid hematin Method

## Slide 3
Principle: Blood is mixed with N/10 HCl resulting in the conversion of Hb to acid hematin which is brown in color. The solution is diluted till it’s color matches with the brown colored glass of the comparator box. The concentration of Hb is read directly.
Hemoglobin + (0.1 N) HCl Acid hematin (brown colour)
The brown color of compound is matched against a brown glass standard in a comparator.

## Slide 4
Equipment required
Hemocytometer which consists of:
1. comparator box which has brown colored glass on either side
2. Hb pipette which is marked up to 20mm3(0.02ml blood)
3. Tube with markings of Hb on one side
4. glass rod
5. dropper

## Slide 6
Reagents required
N/10 HCl
Distilled water
Sample:
Venous blood collected in EDTA as described earlier

## Slide 7
Procedure
1. Placed 0.1(N)HCl acid in the Sahli’s tube up to the lowest mark 20% by using a Pasteur pipette
2. Pipette 0.02 ml of blood in a Hb-pipette and added with the 0.1(N)HCl acid present in the Sahli’s tube. Mixed well and wait for 10 minutes.
3. Diluted the solution with distilled water by adding few drops at a time carefully and diluted the solution, until the colour matches with the glass comparator present in the haemometer.
4. The colour matching should be done only against natural day light. The level of the fluid is noted at its lower meniscus and the reading corresponding to this level on the scale is recorded in gm/dl.

## Slide 8
Advantages
Easy to perform
Quick
Inexpensive
Can be used as a bedside procedure
Does not require technical expertise

## Slide 9
Disadvantages
Less accurate.
All hemoglobins (oxyhemoglobin, sulphemoglobin) are not converted to acid hematin and hence the value of Hb obtained is less than the actual value.
The color of acid hematin develops slowly.
Color of acid hematin fades with time and dilution must be done exactly after 10 min when the color development is maximum
Individual variation in matching of color is seen.

## Slide 10: Hemoglobin Interpretation
A. Increased values:
Physiological
High attitude.
Young age.
Pathological
Dehydration.

## Slide 11
B. Decreased values :
Physiological
Fluid therapy.
Pathological
Anemia.
Hemorrhage.
Blood parasites.
Malignant tumors.