## Slide 1: Fundamental of Control Engineering
Time Response Analysis Lecure-6

## Slide 2: Time Response Analysis
1- First step in analysing any control systems is to derive its mathematical model.
2- In analyzing and designing any control system we must have a basis of performance comparison with different control systems
3- This basis may be setup by specifying particular test input signals and by comparing the responses of various control systems to these input signals.
4- System is effected by changing the input test signal or its initial conditions.
5-

## Slide 3: Time Response Analysis
5- Typical test signals which commonly used in testing are of the type of: -Step functions - Ramp function - Impulse functions and Sinusoidal functions.
6- Time response analysis can be performed only for stable systems.
7- Time response of any system consists from Transient response and steady- state response.
8- Stability and steady state error are the most important characteristics in any control system.

## Slide 4: Definition of Pole and Zero
Consider the transfer function F(s):
The system response is given by:
The poles are the values of s for which the denominator A(s) = 0.
The zeros are the values of s for which the numerator B(s) = 0.
Numerator polynomial
Denominator polynomial

## Slide 5: Effect of Pole Locations
The impulse response will be an exponential function:
When σ > 0, the pole is located at s < 0,
 The exponential expression y(t) decays.
 Impulse response is stable.
When σ < 0, the pole is located at s > 0,
 The exponential expression y(t) grows with time.
 Impulse response is referred to as unstable.
A form of first-order transfer function
How?
Chapter 3
Dynamic Response
Consider the transfer function F(s):

## Slide 6: Effect of Pole Locations
PFE
The terms e–t and e–2t, which are stable, are determined by the poles at s = –1 and –2. This is true for more complicated cases as well.
In general, the response of a transfer function is determined by the locations of its poles.
Example:
Find the impulse response of H(s),
Chapter 3
Dynamic Response

## Slide 7: Effect of Pole Locations
Time function of impulse response assosiated with the pole location in s-plane
LHP
RHP
LHP : left half-plane
RHP : right half-plane
Chapter 3
Dynamic Response

## Slide 8: Representation of a Pole in s-Domain
The position of a pole (or a zero) in s-domain is defined by its real and imaginary parts, Re(s) and Im(s).
In rectangular coordinates, the complex poles are defined as (–s ± jωd).
Complex poles always come in conjugate pairs.
A pair of complex poles
Chapter 3
Dynamic Response

## Slide 9: Representation of a Pole in s-Domain
The denominator corresponding to a complex pair will be:
On the other hand, the typical polynomial form of a second-order transfer function is:
Comparing A(s) and denominator of H(s), the correspondence between the parameters can be found:
ζ : damping ratio
ωn : undamped natural frequency ωd : damped frequency
Chapter 3
Dynamic Response

## Slide 10: Representation of a Pole in s-Domain
Previously, in rectangular coordinates, the complex poles are at (–s ± jωd).
In polar coordinates, the poles are at (ωn, sin–1ζ), as can be examined from the figure.
Chapter 3
Dynamic Response

## Slide 11: Unit Step Resonses of Second-Order System
Chapter 3
Dynamic Response

## Slide 12: Effect of Pole Locations
Example:
Find the correlation between the poles and the impulse response of the following system, and further find the exact impulse response.
Since
The exact response can be otained from:
Chapter 3
Dynamic Response

## Slide 13: Effect of Pole Locations
To find the inverse Laplace transform, the righthand side of the last equation is broken into two parts:
Damped sinusoidal oscillation
Chapter 3
Dynamic Response

## Slide 14: Time Domain Specifications
Specification for a control system design often involve certain requirements associated with the step response of the system:
Delay time, td, is the time required for the response to reach half the final value for the very first time.
Rise time, tr, is the time needed by the system to reach the vicinity of its new set point.
Settling time, ts, is the time required for the response curve to reach and stay within a range about the final value, of size specified by absolute percentage of the final value.
Overshoot, Mp, is the maximum peak value of the response measured from the final steady-state value of the response (often expressed as a percentage).
Peak time, tp, is the time required for the response to reach the first peak of the overshoot.
Chapter 3
Dynamic Response

## Slide 15: Time Domain Specifications
Chapter 3
Dynamic Response

## Slide 16: First-Order System
The step response of first-order system in typical form:
is given by:
t : time constant
For first order system, Mp and tp do not apply
Chapter 3
Dynamic Response

## Slide 17: Second-Order System
is given by:
Chapter 3
Dynamic Response
The step response of second-order system in typical form:

## Slide 18: Second-Order System
Time domain specification parameters apply for most second-order systems.
Exception: overdamped systems, where ζ > 1 (system response similar to first-order system).
Desirable response of a second-order system is usually acquired with 0.4 < ζ < 0.8.
Chapter 3
Dynamic Response

## Slide 19: Rise Time
The step response expression of the second order system is now used to calculate the rise time, tr,0%–100%:
Since , this condition will be fulfilled if:
or,
φ
tr is a function of ωd
Chapter 3
Dynamic Response

## Slide 20: Settling Time
Using the following rule:
The step response expression can be rewritten as:
with:
where:
ts is a function of ζ
Chapter 3
Dynamic Response

## Slide 21: Settling Time
The time constant of the envelope curves shown previously is 1/ζωn , so that the settling time corresponding to a certain tolerance band may be measured in term of this time constant.
Chapter 3
Dynamic Response

## Slide 22: Peak Time
When the step response y(t) reaches its maximum value (maximum overshoot), its derivative will be zero:
Chapter 3
Dynamic Response

## Slide 23: Peak Time
≡0
At the peak time,
Since the peak time corresponds to the first peak overshoot,
tp is a function of ωd
Chapter 3
Dynamic Response

## Slide 24: Maximum Overshoot
Substituting the value of tp into the expression for y(t),
if y(∞) = 1
Chapter 3
Dynamic Response

## Slide 25: Example 1: Time Domain Specifications
Example:
Consider a system shown below with ζ = 0.6 and ωn = 5 rad/s. Obtain the rise time, peak time, maximum overshoot, and settling time of the system when it is subjected to a unit step input.
After block diagram simplification,
Standard form of second-order system
Chapter 3
Dynamic Response

## Slide 26: Example 1: Time Domain Specifications
In second quadrant
Chapter 3
Dynamic Response

## Slide 27: Example 1: Time Domain Specifications
Check y(∞) for unit step input, if
Chapter 3
Dynamic Response

## Slide 28: Example 1: Time Domain Specifications
Chapter 3
Dynamic Response

## Slide 29: Example 2: Time Domain Specifications
Example:
For the unity feedback system shown below, specify the gain K of the proportional controller so that the output y(t) has an overshoot of no more than 10% in response to a unit step.
Chapter 3
Dynamic Response

## Slide 30: Example 2: Time Domain Specifications
: K = 2
: K = 2.8
: K = 3
Chapter 3
Dynamic Response